## Slide 1: Reaction Forces and Moments

## Slide 2: Free Body Diagram Reactions
Different types of support reactions
Cable, rope, or chain
Pin
Roller
Built-in end – Cantilever

## Slide 3
Notes: cantilever bridge – a bridge in which each span is constructed from cantilevers built out sideways from piers. Cantilevers must be firmly anchored on one side in order to hold up the necessary weight on the free standing side and avoid shear stress. A common example of a small cantilever is a diving board. One side is firmly attached to the ground so that the other side can hold a person’s weight suspended over the water. Cantilevers must resist tension in the upper supports and compression in the lower

## Slide 4: Cable Support Examples
Cable
Chain
Rope

## Slide 5
Pin Supports

## Slide 6
Roller Support

## Slide 7: Pin Support
Pin – Replaced with TWO reaction forces, one vertical (y) and one horizontal (x).
A
RAx
RAy
A

## Slide 8: Roller Support
Roller – Replaced with ONE reaction force, perpendicular to surface
A
A
RAy

## Slide 9: Common Support Reactions
Beams and truss bridges are usually supported with one pin support and one roller support. This is called a simply supported object.
FBD for the simply supported beam.
A
B
RAx
RAy
RBy

## Slide 10: Truss Bridge
Supported with a pin at one end and a roller at the other
Draw the FBD of the entire truss bridge.
A
B
C
D
E
500 lb

## Slide 11: Truss Bridge FBD
FBD of the entire truss bridge
B
C
D
E
500 lbf
RAx
RAy
RCy

## Slide 12: Moment
The moment of a force is a measure of the tendency of the force to rotate the body upon which it acts.
FORCE
Notes: The force applied to drive the bolt produces a measurable moment, and the wrench rotates about the axis of the bolt.

## Slide 13: Terminology
FORCE
= F
pivot
distance
= D
lever arm
The distance must be perpendicular to the force.

## Slide 14: Moments Formula
FORCE
= F
pivot
Moment
M
M = F x D
distance
= D

## Slide 15: Units for Moments
 | Force | Distance | Moment
English Customary | Pound force (lbf) | Foot (ft) | lb-ft
SI | Newton (N) | Meter (m) | N-m

## Slide 16: Rotation Direction
In order to add moments, it is important to know if the direction is clockwise (CW) or counterclockwise (CCW).
CCW is positive
CW is negative

## Slide 17: Moment Calculations
Wrench
FORCE
F = 20. lb
D = 9.0 in.
M = -(F x D)
D = 9.0 in. = .75 ft
M = -(20. lb x .75 ft)
M = -15 lb-ft
(15 lb-ft clockwise)
¯

## Slide 18: Moment Calculations
Longer Wrench
FORCE
F = 20. lb
D = 1.0 ft
M = -(F x D)
M = -(20. lb x 1.0 ft)
M = -20. lb-ft
¯

## Slide 19: Moment Calculations
L - Shaped Wrench
FORCE
F = 20. lb
D = 3 in. = .25 ft
M = -(F x D)
M = -(20. lb x .25 ft)
M = -5 lb-ft
¯
3 in.
D = 1.0 ft
Notes: If you have a vertical force, you are looking for a horizontal distance to the pivot.
If you have a horizontal force, you are looking for a vertical distance to the pivot.

## Slide 20: Moment Calculations
Z - Shaped Wrench
FORCE
F = 20. lb
D = 8 in. + 10 in. = 1.5 ft
M = -(F x D)
M = -(20. lb x 1.5 ft)
M = -30. lb-ft
¯
8 in.
9 in.
10. in.
Notes: Given a vertical force, look for a horizontal distance.

## Slide 21: Moment Calculations
D = r = 50. cm = 0.50 m
M = F x D
M = 100 N x 0.50 m
M = 50 N-m
Wheel and Axle
F = 100 N
r = 50. cm
+
Notes: Given a vertical force, look for a horizontal distance.

## Slide 22: Determining Equilibrium
The sum of all moments about any point or axis is zero.
ΣM = 0
M1 + M2 + M3 . . . = 0
Notes: Moments
Principles of EngineeringTM
Unit 4 – Lesson 4.1 - Statics

## Slide 23: Moment Calculations
See-Saw

## Slide 24: Moment Calculations
ΣM = 0
M1 = M2
F1 x D1 = F2 x D2
25 lb x 4.0 ft = - 40. lb x D2
100 lb-ft = - 40. lb x D2
See-Saw
F1 = 25 lb
F2 = 40. lb
D1 = 4.0 ft
D2 = ? ft
- 40. lb - 40. lb
2.5 ft = D2
+
¯

## Slide 25: Moment Calculations
ΣM = 0
MB = MC
RBy x DAB = FC x DAC
RBy x 10.00 ft = 35.0 lb x 3.00 ft
RBy x 10.00 ft = 105 lb-ft
Loaded Beam
DAB = 10.00 ft
DAC= 3.00 ft
A
C
B
RAy
FC = 35.0 lb
RBy
10.00 ft 10.00 ft
RBy = 10.5 lb
RAy + RBy = 35.0 lb
RAy = 35.0 lb – 10.5 lb = 24.5 lb
Select A as the pivot location. Solve for RBy